APT GUIDELINES

ON

TECHNICAL CONDITIONS FOR THE USE OF MOBILE PHONES ONBOARD AIRCRAFT

No. APT/AWG/OP-02 (Rev.2)

Edition: September 2011

Adopted by

The 6th APT Wireless Forum Meeting

31 March – 3 April 2010

Danang, Vietnam S. R.

1st Revision at

The 9th APT Wireless Forum Meeting

13 – 16 September 2010

Seoul, Republic of Korea

2nd Revision at

The 11th APT Wireless Group Meeting

14 – 17 September 2011

Chiang Mai, Thailand

|  | ASIA-PACIFIC TELECOMMUNITY |  |
| --- | --- | --- |
|  | The APT Wireless Group |  |

Source: AWG-11/OUT-09(Rev.1)

APT GUIDELINES ON TECHNICAL CONDITIONS FOR THE USE OF MOBILE PHONES ONBOARD AIRCRAFT

This document defines the guidelines on technical conditions for the use of mobile phones onboard aircraft. The technical guidelines have been defined by analyzing the frequencies and technologies present in the Asia Pacific region and proposing the maximum permitted power possible in a technology neutral manner.

This guidelines document does not presume that an administration has authorised the service. The guidelines presented here are provided as supporting information for national administrations when considering the technical conditions of the onboard cellular service.

The technical guidelines defined in step 4 have been created from the following steps:

- Step One: Frequency bands and technologies covered in the Asia Pacific Region
Identification of all spectrum bands and technologies operating in the various countries/regions of the Asia Pacific Region. The analysis is based on publicly available information on the cellular frequencies used in the Asia Pacific region, and consequently may need to be updated.

- Step Two: Derivation of control bands, connectivity bands 
Identification of the bands required to control and the potential bands that could operate an onboard service, based on the spectrum band and technologies found in step 1. It is highlighted that connectivity can only occur if the cellular system has a pre defined roaming infrastructure, this reduces the possibility of offering connectivity service to only MAP based (e.g. GSM or UMTS) and IS 41 based (e.g.cdma2000) cellular networks.

- Step Three: Derivation of power limits 
The third section defines the criteria for harmful interference to receivers on the ground and the associated power limit to conform to this criteria.

- Step Four: The Guidelines on Technical Conditions for the Use of Mobile Phones Onboard Aircraft 
Proposed AWF Guidelines On Technical Conditions For The Use Of Mobile Phones Onboard Aircraft.

The  following provides the technical a guideline for national administrations to use when considering the technical conditions for the use of mobile phones onboard aircraft framework.

1: Step One: Frequency bands and technologies covered in the Asia Pacific Region

The following table provides the analysis of technologies and frequencies currently deployed in the Asia Pacific region. The information is based on publicly available information. Where a country/region is missing or information is not present the authors would request to be updated.

| Technology | Frequency | Band |
| --- | --- | --- |

| Australia |
| --- |
| CDMA800 / UMTS (WCDMA) 800 | 825 – 845 / 870 – 890 | A |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1785 / 1805 -1880 | C |
| UMTS(WCDMA) | 1920 – 1980 / 2110 -2170 | E |

| Bangladesh |
| --- |
| CDMA800 | 824 – 849 / 869 – 894 | A |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1785 / 1805 -1880 | C |
| UMTS (WCDMA) | 1920 – 1980 / 2110 -2170 | E |

| Bhutan |
| --- |
| GSM900 | 890 – 915 / 935 – 960 | B |

| Brunei Darussalam |
| --- |
| GSM900 | 890 – 915 / 935 – 960 | B |
| UMTS(WCDMA) | 1920 – 1980 / 2110 -2170 | E |

| Cambodia |
| --- |
| CDMA450 | 450 – 460 / 460 - 470– | F |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1785 / 1805 -1880 | C |

| China (People’s Republic of China) |
| --- |
| CDMA800 | 825 – 835 / 870 – 880 | A |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1755 / 1805 -1850 | C |
| CDMA2000 | 1920-1935/2110-2125 | E |
| UMTS(WCDMA) | 1940-1955/2130-2145 | E |
| TD-SCDMA | 1880 – 1900 TDD | M2 |
| TD-SCDMA | 2010 – 2025 TDD | N |
| TD-SCDMA | 2300 – 2400 TDD | P |

| Guam |
| --- |
| CDMA800 / TDMA800 | 824 – 849 / 869 – 894 | A |
| CDMA1900 / GSM1900 | 1850 – 1910 / 1930 – 1990 | D |

| India (Republic of) |
| --- |
| CDMA800 | 824 – 849 / 869 – 894 | A |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1785 / 1805 -1880 | C |

| Indonesia (Republic of) |
| --- |
| CDMA800 | 825 – 845 / 870 – 890 | A |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1785 / 1805 -1880 | C |
| PCS1900 | 1903.125-1910/1983.125-1990 | D |
| UMTS(WCDMA)2100 | 1920 – 1980 / 2110 -2170 | E |
| CDMA450 | 450-457.5 / 460-467.5 | F |

| Japan |
| --- |
| UMTS(WCDMA)2100/CDMA 2000 | 1920 – 1980 / 2110 -2170 | E |
| E-UTRA(LTE) | 1950 – 1960 / 2140 – 2150 | E2 |
| PDC800 | 940 – 948 / 810 – 818 930 – 940 / 875 – 885 | G |
| UMTS (WCDMA)800 / CDMA800 | 815 – 845 / 860 – 890 | I |
| CDMA800 | 898 – 901 / 843 – 846 915 – 925 / 860 – 870 | J |
| UMTS(WCDMA)1500/CDMA1500 | 1427.9 – 1437.9 / 1475.9 – 1485.9 | K |
| UMTS (WCDMA)1700 / CDMA1700 | 1754.9 – 1764.9 / 1849.9 – 1859.9 1769.9 – 1784.9 / 1864.9 – 1879.9 | L |
| PHS | 1884.5 - 1918.4 (TDD) | M |
| BWA systems (WiMAX,XGP) | 2545 – 2575 (TDD) 2595 – 2625 (TDD) | O |

| Korea (Democratic People’s Republic of) |
| --- |
| GSM900 | 890 – 915 / 935 – 960 | B |

| Korea (Republic of) |
| --- |
| CDMA800 | 824 – 849 / 869 – 894 | A |
| CDMA1800 | 1750 – 1780 / 1840 – 1870 | C |
| UMTS(WCDMA)2100 | 1920 – 1980 / 2110 -2170 | E |
| Mobile WiMAX (WiBro) | 2300 – 2400 | P2 |

| Laos |
| --- |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1785 / 1805 -1880 | C |

| Macau |
| --- |
| CDMA800 | 825-845/870-890 | A |
| GSM900 | 890 – 915 / 935 – 960 | B |
| GSM1800 | 1710 – 1785 / 1805 -1880 | C |
| UMTS(WCDMA)2100 | 1920 – 1980 / 2110 -2170 | E |

| Malaysia |
| --- |
| EGSM900 | 880 – 915/ 925 – 960 | B2 |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| UMTS(WCDMA)2100 | 1920 – 1980/ 2110 -2170 | E |
| BWA | 2300-2400 | P2 |

| Mongolia |
| --- |
| CDMA800 | 824 – 849 / 869 – 894 | A |
| GSM900 | 890 – 915/ 935 – 960 | B |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| CDMA450 | 450 - 460 / 460 – 470 | F |

| Myanmar (The Union of) |
| --- |
| CDMA800 / TDMA800 | 824 – 849 / 869 – 894 | A |
| GSM900 | 890 – 915/ 935 – 960 | B |

| New Zealand |
| --- |
| W-CDMA 850/CDMA-2000 | 825 – 840 / 870 – 885 | A |
| GSM900/WCDMA-900 | 890 – 915/ 935 – 960 | B |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| UMTS(WCDMA)2100 | 1920 – 1980/ 2110 -2170 | E |
| BWA | 2300-2400 | P2 |

| Northern Mariana Islands |
| --- |
| CDMA800 / GSM 800 | 824 – 849 / 869 – 894 | A |
| GSM1900 | 1850-1910/ 1930-1990 | D |

| Pakistan (Islamic Republic of) |
| --- |
| TDMA800 | 824 – 849 / 869 – 894 | A |
| GSM900 | 890 – 915/ 935 – 960 | B |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |

| Papua New Guinea |
| --- |
| EGSM900 | 880 – 915/ 925 – 960 | B2 |

| Philippines (Republic of the) |
| --- |
| 3G(WCDMA) | 870-880/825-835 | A |
| GSM900 | 890 – 915/ 935 – 960 | B |
| EGSM | 880-890/925-935 | B2 |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| CDMA 1900 | 1900 – 1910 / 1980 – 1990 | D |
| UMTS(WCDMA)2100 | 1920 – 1980/ 2110 -2170 | E |

| Singapore |
| --- |
| EGSM900 | 880 – 915/ 925 – 960 | B2 |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| UMTS(WCDMA)2100 | 1920 – 1980/ 2110 -2170 | E |

| Sri Lanka |
| --- |
| GSM900 | 890 – 915/ 935 – 960 | B |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |

| Taiwan |
| --- |
| CDMA800 | 824 – 849 / 869 – 894 | A |
| GSM900 | 890 – 915/ 935 – 960 | B |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| UMTS(WCDMA)2100 | 1920 – 1980/ 2110 -2170 | E |

| Thailand |
| --- |
| CDMA800 / UMTS 800 | 824 – 849 / 869 – 894 | A |
| GSM 900/ UMTS 900 | 897.5 – 915/ 942.5 - 960 | B3 |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| UMTS(WCDMA)2100 | 1920 – 1980/ 2110 -2170 | E |

| Tonga |
| --- |
| GSM900 | 890 – 915/ 935 – 960 | B |

| Vietnam (Socialist Republic of) |
| --- |
| CDMA800 | 829 – 845 / 874 – 890 (824 – 829 / 869 – 894 as of 2010) | A |
| GSM900 | 890 – 915/ 935 – 960 | B |
| GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| IMT 2000 | 1920 – 1980/ 2110 -2170 | E |
| CDMA 450 | 453.08 – 457.37 / 465.08 – 467.37 | F |

The information contained in the tables above merely reflect the current deployment of terrestrial cellular networks for each nation. The inclusion of a country/region within the tables above does not presume that the onboard cellular system has been authorised by that administration.

2: Step two: Derivation of control and connectivity bands used in Asia Pacific Region

2.1 Cellular frequency bands and technologies used in the Asia Pacific region

Based on the analysis in Step 1 above the following cellular bands and technologies have been identified in the Asia Pacific region.

| Technology | Frequency (UL/DL) | Band |
| --- | --- | --- |
| CDMA800 / TDMA 800/ GSM 800/ UMTS 800 | 824 – 849 / 869 – 894 | A |
| GSM900 | 890 – 915/ 935 - 960 | B |
| EGSM 900 | 880 – 915/ 925 - 960 | B2 |
| GSM 900/ UMTS 900 | 897.5 – 915/ 942.5 - 960 | B3 |
| CDMA 1800 / GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| CDMA 1900 / GSM1900 | 1850-1910/ 1930-1990 | D |
| UMTS (WCDMA)/ CDMA 2000 | 1920 – 1980/ 2110 -2170 | E |
| E-UTRA(LTE) | 1950 – 1960 / 2140 – 2150 | E2 |
| CDMA450 | 450-460/ 460-470 | F |
| PDC 800 | 940 – 948 / 810 – 818 930 – 940 / 875 – 885 | G |
| UMTS (WCDMA) 800/ CDMA 800 | 815 - 845 / 860 - 890 | I |
| CDMA800 | 898 - 901 / 843 - 846 915 – 925 / 860 – 870 | J |
| UMTS (WCDMA)1500/CDMA1500 | 1427.9 - 1437.9 / 1475.9 - 1485.9 | K |
| UMTS(WCDMA)1700 | 1754.9 - 1764.9 / 1849.9 - 1859.9 1769.9 – 1784.9 / 1864.9 – 1879.9 | L |
| PHS | 1884.5 - 1918.4 (TDD) | M |
| TD-SCDMA | 1880 – 1900 (TDD) | M2 |
| TDD mobile communication systems | 2010 – 2025 (TDD) | N |
| BWA systems (WiMAX,XGP) | 2545 – 2575 (TDD) 2595 – 2625 (TDD) | O |
| TD-SCDMA | 2300 – 2400 (TDD) | P |
| Mobile WiMAX (WiBro) | 2300 – 2400 (TDD) | P2 |

In order to operate an onboard system, a mechanism must exist to ensure that mobile phones onboard the aircraft cannot detect terrestrial cellular networks overflown. It is highlighted that a mobile will only transmit if it can identify a mobile network. Therefore if a country/region has not deployed a particular cellular frequency band (i.e. 450 MHz) then the onboard cellular system will not need to control that band.

Consideration may also be required for non cellular wireless technologies when deployed in the same frequency band. In particular where there is a mix of both cellular wireless and non cellular wireless terrestrial deployed systems in the same band.

2.2 Mapping of cellular frequency bands and technologies to countries/regions

Based on the analysis in step 1 the following bands and technologies of public mobile communications systems per country/region have been identified in the Asia Pacific region

| Country / Region | Band Used | Country / Region | Band Used |
| --- | --- | --- | --- |
| Australia | A, B, C, E | Bangladesh | A, B, C |
| Bhutan | B | Brunei Darussalam | B, E |
| Cambodia | B, C, E, F | China (People’s Republic of) | A, B, C, E,M2, N ,P |
| Guam | A, D | India (Republic of) | A, B, C |
| Indonesia (Republic of) | A, B, C ,D,E, F | Japan | E, E2,G, I, J, K, L, M, O |
| Korea (Democratic People’s Republic of) | B | Korea (Republic of) | A, C, E, P2 |
| Laos | B, C | Macau | A, B, C, E |
| Mongolia | A, B | Malaysia | B2, C, E,P2 |
| New Zealand | A, B, C, E,P2 | Myanmar (The Union of) | A, B |
| Pakistan (Islamic Republic of) | A, B, C | Northern Mariana Islands | A, D |
| Philippines (Republic of the) | A,B, B2,C, D, E | Papua New Guinea | B2 |
| Sri Lanka | B, C | Singapore | B2, C, E |
| Thailand | A,B3, C, E | Taiwan | A, B, C, E |
| Vietnam (Socialist Republic of) | A, B, C, E, F | Tonga | B |

The information contained in the tables above reflects the current deployment of terrestrial cellular networks for each nation. The inclusion of a country/region within the tables above does not presume that the onboard cellular system has been authorised by that administration.

2.3 Possible connectivity frequency bands and technologies for offering connectivity

Based on the condition that connectivity inside the cabin can only be achieved using a mobile system which has an established roaming functionality (i.e. MAP (e.g. GSM and /or UMTS) or IS 41 (e.g. cdma2000) based networks) then the following technologies and bands can be used in the Asia Pacific region

| Technology | Frequency (UL/DL) | Band |
| --- | --- | --- |
| CDMA800 / GSM 800 | 824 – 849 / 869 894 | A |
| GSM900 | 890 – 915/ 935 960 | B |
| CDMA 1800 / GSM1800 | 1710 – 1785/ 1805 -1880 | C |
| CDMA 1900 / GSM1900 | 1850-1910/ 1930-1990 | D |
| UMTS (WCDMA) | 1920 – 1980/ 2110 -2170 | E |

3: Step three: Derivation of Power limits of the system

The following proposes the criteria for harmful interference to terrestrial receivers in order to define the limiting power conditions of an onboard cellular system.

3.1 The criteria for harmful interference

In order not to cause harmful interference to terrestrial networks it is proposed that the Mobile Phone onboard aircraft system shall not cause more than a 1 dB rise in the effective noise floor of the receiving “victim” terminal receiver on the ground.

The effective noise floor of the receiver is based on the absolute lowest level that a receiver could possibly work; i.e. the physical limit for thermal noise (kBT (Boltzmans constant * the bandwidth * temperature (in Kelvin)) plus the additional losses in the circuitry of the device (the so called noise figure).

This figure is based on input from the international standards group 3GPP (Third Generation Project Partnership, see http://www.3gpp.org)) which defines 3rd Generation mobile systems and comprises of operators and suppliers in the mobile industry. Further this criteria was used as the basis for the technical annex of the European ECC Decision (06)07. 3GPP provided the following clarification:

- 3GPP proposes the noise figure for a terminal is 7 dB thus providing an effective noise floor of the terminal equal to kBT + noise figure (= 7 dB).

- 3GPP proposes the noise figure for the network radio base station is 4 dB thus providing an effective noise floor of the base station equal to kBT + noise figure (= 4 dB).

- 3GPP endorsed the criteria of 1 dB increase in the effective noise floor for the definition of harmful interference for the onboard mobile system. A 1 dB increase in the effective noise floor of the receiver equates to the 
interfering signal (I) = Effective Noise floor (N) – 6 dB.

3.2 Power limits as a function of frequency and height above ground

International developments for the mobile phones service in aircraft define a minimum height above the ground to which the service can be activated. In some countries this limit has been set at 3,000 m (10,000 feet) which coincides with the distinction between the definition of critical and non critical phases of flight in the aeronautical industry.

In order to have a cellular technology neutral approach, a power level parameter given as dBm/Hz is used. However the permitted power emanating outside an aircraft will be dependent on both the solution proposed and the properties of the aircraft itself. Therefore in order to provide an aircraft agnostic solution, power levels must be defined as power emitted by the aircraft. Consequently, in order to provide a technology neutral solution the power maximum limits are defined as a function of both frequency and height above the ground in order to satisfy the criteria stated in 3.1 above.

Given the different characteristics between the base station receiver and the mobile station receiver, two sets of limits are required. The following table proposes the maximum power level an aircraft can transmit in the downlink direction i.e. into the receiver of the mobile phone on the ground and assuming a minimum height the service can be activated as 3,000 metres above the ground.

| Height above ground (m) | Maximum E.i.r.p. permitted outside the aircraft in dBm/Hz |
| --- | --- |
|  | Band F: 450 MHz | Band A & G: 800 MHz | Band B: 900 MHz | Band H: 1400 MHz | Band C: 1800 MHz | Band D: 1900 MHz | Band E: 2 GHz |
| 3000 | -78.0 | -72.5 | -72.0 | -68.5 | -66.0 | -65.5 | -65.0 |
| 4000 | -75.5 | -70.0 | -69.5 | -65.5 | -63.5 | -63.0 | -62.5 |
| 5000 | -73.5 | -68.0 | -67.5 | -64.0 | -61.5 | -61.0 | -60.5 |
| 6000 | -72.0 | -66.5 | -66.0 | -62.0 | -60.0 | -59.5 | -59.0 |
| 7000 | -71.5 | -65.1 | -64.5 | -61.0 | -60.0 | -58.0 | -58.0 |
| 8000 | -69.5 | -64.0 | -63.5 | -60.0 | -57.5 | -57.0 | -56.5 |
| 9000 | -68.5 | -63.0 | -62.5 | -59.0 | -56.5 | -56.0 | -55.5 |
| 10000 | -67.5 | -62.0 | -61.5 | -58.0 | -55.5 | -55.0 | -54.5 |

It should be noted that the proposed power limits defined in the table above are dependant on the elevation angle at the victim terminal on the ground. The values contained in the table are for the case where the victim terminal is directly below the aircraft given that a mobile phone antenna is assumed to be omni-directional.

The following table proposes the maximum power level an aircraft can transmit in the uplink direction i.e. into the receiver of the base station on the ground and assuming a minimum height the service can be activated as 3,000 metres above the ground.

| Height above ground (m) | Maximum e.i.r.p permitted, defined outside the aircraft, resulting from a mobile terminal in dBm/Hz |
| --- | --- |
|  | Band: 450 MHz | Band: 800 MHz | Band: 900 MHz | Band: 1800 MHz | Band: 1900 MHz | Band: 2 GHz |
| 3000 | -68.5 | -63.0 | -62.5 | -56.5 | -56.0 | -55.5 |
| 4000 | -66.0 | -60.5 | -60.0 | -54.0 | -53.5 | -53.0 |
| 5000 | -64.0 | -58.5 | -58.0 | -52.0 | -51.5 | -51.0 |
| 6000 | -62.5 | -57.0 | -56.5 | -50.5 | -50.0 | -49.5 |
| 7000 | -61.0 | -55.5 | -55.0 | -49.0 | -48.5 | -48.0 |
| 8000 | -60.0 | -54.5 | -54.0 | -48.0 | -47.5 | -47.0 |
| 9000 | -59.0 | -53.5 | -53.0 | -47.0 | -46.5 | -46.0 |
| 10000 | -58.0 | -52.5 | -52.0 | -46.0 | -45.5 | -45.0 |

For base stations on the ground the worst case scenario is the combination of the antenna vertical pattern and the free space path loss. By using the vertical pattern derived from the International Telecommunications Union Recommendations (ITU R) F.1336-1, it follows that this occurs at an angle of 2 degrees from the horizontal. It should be noted that the limits define in the table above are dependant on the elevation angle at the victim base station on the ground. The values contained in the table correspond to conformance to the harmful interference criteria at an angle of elevation of 2°.

Step 4 - TECHNICAL GUIDELINES

# Proposed Technical conditions for mobile phone systems onboard aircraft

| Nr. | Parameter | Description | Comments | Status |
| --- | --- | --- | --- | --- |
| 1 | Frequency band | Band A: 824 – 849 / 869 – 894 Band B: 890 – 915/ 935 – 960 Band B2: 880 – 915/ 925 – 960 Band B3: 897.5 – 915/ 942.5 - 960Band C: 1710 – 1785/ 1805 -1880 Band D: 1850-1910/ 1930-1990 Band E: 1920 – 1980/ 2110 -2170 Band E2: 1950 – 1960 / 2140 – 2150 Band F: 450-460/ 460-470 Band G: 940 - 948 / 810 – 818 930 - 940 / 875 - 885 Band I: 815 - 845 / 860 - 890 Band J: 898 - 901 / 843 – 846 915 – 925 / 860 - 870 Band K: 1427.9 - 1437.9 / 1475.9 - 1485.9 Band L: 1754.9 - 1764.9 / 1849.9 - 1859.9 1769.9 – 1784.9 / 1864.9 – 1879.9 Band M: 18845.-1918.4 (TDD) Band M2: 1880 – 1900 (TDD) Band N: 2010 – 2025 (TDD) Band O: 2545 - 2575 (TDD) 2595 – 2625 (TDD) Band P: 2300 – 2400 (TDD) Band P2: 2300 – 2400 (TDD) | The downlink frequency of the bands A, B, B2, C, D, E, F, G, H, I, J, K, and L as well as the complete bands of Band M, N, O, P and P2 will have to be controlled within the cabin depending on which country/region the service is operated in as defined in table 3. Only bands A, B, C, D and E can be used for onboard cellular system on the condition that the system controls onboard terminals to transmit within the power limits defined in table 4. | C |
| 2 | Radio service | Mobile Service |  | M |
| 3 | Application | On-board cellular passenger communication system | GSM standard | C |
|  |  |  | Cdma2000 standard |  |
| 4 | Channelling / modulation | GSM standard |  | C |
|  |  | cdma2000 standard |  |  |
| 5 | Transmit power limit | Maximum permitted e.i.r.p. limits of on-board cellular system are defined outside the aircraft. Authorisation of the use of the system will depend on the fact that the installed system conforms to the limits outside the aircraft defined in Reference Table 3 and Table 4 in order to ensure no harmful interference with terrestrial mobile networks. Below 3000 m all the Mobile phone on-board cellular system will have to be switched off. | The absolute minimum height above ground for any transmission from the system in operation shall be 3000 metres. However, this minimum height requirement could be set higher, in particular: (1) in order to comply with the aircraft base station and onboard mobile phone emission conditions as set out in Reference tables 3 and 4, (2) depending on the terrain and related network deployments in a country/region. | M |
| 6 | Channel occupation rules | GSM standard |  | C |
|  |  | cdma2000 standard |  |  |
| 7 | Duplex direction / separation | GSM standard |  | C |
|  |  | cdma2000 standard |  |  |
| 8 | Additional Requirements to BTS | The aircraft base station shall control the transmit power of all mobile terminals allowed to transmit on the aircraft. The maximum controlled nominal power value for mobiles phones shall be no greater than -53 dBm/ Hz at all stages of communication, including initial access. | For GSM mobiles this is equivalent to a maximum permitted nominal power limit of 0 dBm/ 200KHz For cdma based mobiles consideration will also be required on the number of mobiles transmitting simultaneously For CMDA 2000 mobiles this limit is equivalent to a maximum permitted nominal power limit of 0 dBm/1.25 MHz (assuming 8 dB multiple interference factor in the aircraft) | M |

Table 1 Minimum requirements set description

C = Conditional requirement depending on country/region overflown and connectivity solution used

M= Mandatory requirement

| Country / Region | Band Used | Country / Region | Band Used |
| --- | --- | --- | --- |
| Australia | A, B, C, E | Bangladesh | A, B, C |
| Bhutan | B | Brunei Darussalam | B, E |
| Cambodia | B, C, E, F | China (People’s Republic of) | A, B, C, E,M2, N ,P |
| Guam | A, D | India (Republic of) | A, B, C |
| Indonesia (Republic of) | A, B, C ,D,E, F | Japan | E, E2,G, I, J, K, L, M, O |
| Korea (Democratic People’s Republic of) | B | Korea (Republic of) | A, C, E, P2 |
| Laos | B, C | Macau | A, B, C, E |
| Mongolia | A, B | Malaysia | B2, C, E,P2 |
| New Zealand | A, B, C, E, P2 | Myanmar (The Union of) | A, B |
| Pakistan (Islamic Republic of) | A, B, C | Northern Mariana Islands | A, D |
| Philippines (Republic of the) | A,B, B2,C, D, E | Papua New Guinea | B2 |
| Sri Lanka | B, C | Singapore | B2, C, E |
| Thailand | A,B3, C, E | Taiwan | A, B, C, E |
| Vietnam (Socialist Republic of) | A, B, C, E, F | Tonga | B |

Table 2: Country by country (region) cellular bands deployment in Asia Pacific region

| Height above ground (m) | Maximum E.i.r.p. permitted outside the aircraft in dBm/Hz |
| --- | --- |
|  | Band F: 450 MHz | Band A & G: 800 MHz | Band B & B2: 900 MHz | Band H: 1400 MHz | Band C: 1800 MHz | Band D: 1900 MHz | Band E: 2 GHz |
| 3000 | -78.0 | -72.5 | -72.0 | -68.5 | -66.0 | -65.5 | -65.0 |
| 4000 | -75.5 | -70.0 | -69.5 | -65.5 | -63.5 | -63.0 | -62.5 |
| 5000 | -73.5 | -68.0 | -67.5 | -64.0 | -61.5 | -61.0 | -60.5 |
| 6000 | -72.0 | -66.5 | -66.0 | -62.0 | -60.0 | -59.5 | -59.0 |
| 7000 | -71.5 | -65.1 | -64.5 | -61.0 | -60.0 | -58.0 | -58.0 |
| 8000 | -69.5 | -64.0 | -63.5 | -60.0 | -57.5 | -57.0 | -56.5 |
| 9000 | -68.5 | -63.0 | -62.5 | -59.0 | -56.5 | -56.0 | -55.5 |
| 10000 | -67.5 | -62.0 | -61.5 | -58.0 | -55.5 | -55.0 | -54.5 |

Table 3: Maximum permitted e.i.r.p. by aircraft due to onboard transmitters in downlink bands

(base station transmit) direction

It should be noted that the limits, defined in Table 3, are dependant on the elevation angle of the victim terminal on the ground. The values contained in the table are applicable to the scenario where the victim terminal is directly below the aircraft.

| Height above ground (m) | Maximum e.i.r.p permitted, defined outside the aircraft, resulting from a mobile terminal in dBm/Hz |
| --- | --- |
|  | Band: 450 MHz | Band: 800 MHz | Band: 900 MHz | Band: 1800 MHz | Band: 1900 MHz | Band: 2 GHz |
| 3000 | -68.5 | -63.0 | -62.5 | -56.5 | -56.0 | -55.5 |
| 4000 | -66.0 | -60.5 | -60.0 | -54.0 | -53.5 | -53.0 |
| 5000 | -64.0 | -58.5 | -58.0 | -52.0 | -51.5 | -51.0 |
| 6000 | -62.5 | -57.0 | -56.5 | -50.5 | -50.0 | -49.5 |
| 7000 | -61.0 | -55.5 | -55.0 | -49.0 | -48.5 | -48.0 |
| 8000 | -60.0 | -54.5 | -54.0 | -48.0 | -47.5 | -47.0 |
| 9000 | -59.0 | -53.5 | -53.0 | -47.0 | -46.5 | -46.0 |
| 10000 | -58.0 | -52.5 | -52.0 | -46.0 | -45.5 | -45.0 |

Table 4: Maximum permitted e.i.r.p. by aircraft due to onboard transmitters in uplink bands

(mobile phone transmit) direction

It should be noted that the limits, defined in table 4, are dependant on the elevation angle of the victim base station receiver on the ground. The values contained in the table correspond to worse case conformance criteria parameters to ensure no harmful interference criteria (calculated at an angle of elevation of 2°).