APT SURVEY REPORT

On

FEMTOCELL

No. APT/AWG/REP-21

Edition: September 2011

Adopted by

The 11th APT Wireless Group Meeting

14 – 17 September 2011

Chiang Mai, Thailand

|  | ASIA-PACIFIC TELECOMMUNITY |  |  |
| --- | --- | --- | --- |
|  | The APT Wireless Group |  |

Source: AWG-11/OUT-05(Rev.1)

APT SURVEY REPORT ON FEMTOCELL

# 1.	Introduction

During the AWF-9 meeting held in Seoul, Korea, September 2010, the Convergence WG (become WG-Service & Application under the new AWG structure) made the questionnaire on Femtocell in APT Region based on the received input contributions (doc. AWF-9-INP-68) and preceded as output (doc. AWF-9-OUT-08). The feedback or answers from administrations supposed be collected and analyzed as a basis for the further study on Femtocell within APT region.

In the previous meetings, convergence working group has also developed following documents:

- Report on the Regulatory Aspect of Fixed Mobile Convergence (doc. AWF-7/OUT-07 and adopted as APT/AWF/REP-09)

- Draft “Report of the Standardization Progress of Fixed Mobile Convergence” (doc. AWF-9/OUT-06), where this document was finalized and approved as AWF report doc. APT/AWF/REP-17

- Working Document Towards Draft report of “FMC Business Model” (doc. AWF-9/TMP-30, AWG-10/TMP-01(Rev.1))

- Working documents towards draft new report on Femtocell (doc. AWG-10/TMP-02)

One of the solutions for fixed-mobile convergence scenario is by utilizing Femtocell, where the femto access point installed in the customer’s house, covers a very small radius and it is connected to the mobile operator infrastructure via residential DSL or cable broadband connections.

Operators in some countries have deployed yet this femtocell-based solution. However, in some other countries it is not developed yet or still under studying.

A femtocell is a small, low cost, low power access point, enabling to access to a network operated wireless network, located in user or private premises.  In term of spectrum, the femtocell shares the licensed wireless spectrum with the macrocell. The femtocell is connected to the operator’s network through an IP broadband backhaul connection such as fibre, DSL or cable.

Figure 1.  High-level Femtocell Network Architecture (source: www.eetimes.com)

Femto Forum uses Femtocell Access Point (FAP) terminology for the femtocell base station while 3GPP uses Home Node B (HNB) for 3G femtocell and Home eNodeB (HeNB) for LTE Femtocell.

As can be seen from Figure 1, Several FAPs are connected to the FAP Gateway (FGW) or H(e)NB Gateway which is a mobile operator’s equipment (usually physically located on mobile operator premises) through which the FAP gets access to mobile operator’s core network.

Regarding the Femtocell questionnaire, one of the objectives of the Convergence Working Group is to study and identify current, emerging and future issues of radio communication that are affected by the convergence of ICT, including fixed-mobile convergence, where the study may include technical, regulatory and business model issues.

2. Summary of the responded questionnaire

Based on the responses received until AWG-11, the responding participants of the questionnaire are:

- Australian Communications and Media Authority (doc. AWG-10-INP-12).

- Japan Ministry of Internal Affairs and Communications (doc. AWG-10-INP-15).

- EMOBILE Inc. Japan (doc. AWG-10-INP-15).

- NTT DOCOMO INC. (doc. AWG-11/INP-18)

- KDDI CORPORATION (doc. AWG-11/INP-18)

- Softbank Mobile Corp, (doc. AWG-11/INP-18)

- Alcatel-Lucent Singapore (doc. AWG-10-INP-19).

- MIIT China (doc. AWG-10/INP-33)

- CMCC (China Mobile Communication Corp) (doc. AWG-10/INP-33)

- China Unicom (doc. AWG-10/INP-33)

- China Telecom (doc. AWG-10/INP-33)

- Huawei Technologies (doc. AWG-10/INP-33)

- Datang Telecom (doc. AWG-10/INP-33)

- ZTE (doc. AWG-10/INP-33)

- Authority for Info-communications Technology Industry of Brunei Darussalam, AITI (doc. AWG-10-INP-66).

- New Zealand Ministry of Economic Development (doc. AWG-10-INP-71)

- 2degrees mobile New Zealand cellular operator (doc. AWG-10-INP-71)

- PT. Telekomunikasi Indonesia (doc. AWG-10-INP-74).

- KCC (doc. AWG-11/INP-34)

- KT Corp (doc. AWG-11/INP-34)

- LG Uplus (doc. AWG-11/INP-34)

- SK Telecom (doc. AWG-11/INP-34)

- LG Electronics, Inc. (doc. AWG-11/INP-34)

- LG-Ericsson (doc. AWG-11/INP-34)

- Samsung Electronics Co., Ltd. (doc. AWG-11/INP-34)

- ETRI (doc. AWG-11/INP-34)

This questionnaire report is divided into four target groups, which are regulators, operators, vendors, and other institutions. Figure 2 illustrate the number of participants on each target groups.

Figure 2. Group of participants

The detailed group of participant are as below:

# For Regulators questionnaire, the responding participants are

- Australian Communications and Media Authority (doc. AWG-10-INP-12).

- Japan Ministry of Internal Affairs and Communications (doc. AWG-10-INP-15).

- Authority for Info-communications Technology Industry of Brunei Darussalam , AITI (doc. AWG-10-INP-66).

- New Zealand Ministry of Economic Development (doc. AWG-10-INP-71).

- MIIT China (doc. AWG-10/INP-33)

- Korea Communication Commission  (doc. AWG-11/INP-34)

# For Operators questionnaire, the responding participants are

- EMOBILE Inc. (doc. AWG-10-INP-15).

- CMCC (doc. AWG-10/INP-33)

- China Unicom (doc. AWG-10/INP-33)

- China Telecom (doc. AWG-10/INP-33)

- New Zealand cellular operator (doc. AWG-10-INP-71)

- PT. Telekomunikasi Indonesia (doc. AWG-10-INP-74)

- KT Corp (doc. AWG-11/INP-34)

- LG Uplus (doc. AWG-11/INP-34)

- SK Telecom (doc. AWG-11/INP-34)

- NTT DOCOMO INC. (doc. AWG-11/INP-18)

- KDDI CORPORATION (doc. AWG-11/INP-18)

- Softbank Mobile Corp, (doc. AWG-11/INP-18)

# For Vendors questionnaire, the responding participants are

- Alcatel-Lucent Singapore (doc. AWG-10-INP-19).

- Huawei Technologies (doc. AWG-10/INP-33)

- Datang Telecom (doc. AWG-10/INP-33)

- ZTE (doc. AWG-10/INP-33)

- LG Electronics, Inc. (doc. AWG-11/INP-34)

- LG-Ericsson (doc. AWG-11/INP-34)

- Samsung Electronics Co., Ltd. (doc. AWG-11/INP-34)

# For other institutions questionnaire, the responding participants is

- ETRI (doc. AWG-11/INP-34)

3. Questionnaire Results

The summary answers of the questionnaires are as follows:

- Femtocell deployment and plan

All of regulators convince that Femtocell deployments and planning has been established and almost all vendors already supplying the related solutions to the telecom market. In spite of that, some operators are still under planning or not intend to deploy Femtocell.

Figure 3. Femtocell deployment and plan

- Type of Femtocell that are deployed and supported

The 3GPP type mostly already in market and supported by regulators and operators.

Figure 4. Type of Femtocell that are deployed and supported

- Spectrum and terminal regulatory that are applied, held and supported

Regulators mostly prefer not to allocate the frequency exclusively and using the existing cellular phone services spectrum (Regulators which are answer “Others”). Regulators also regulate the kind of terminal for Femtocell based on their national standard specification. All operators have frequency exclusive allocation; however, in some countries license issue has not been decided yet and some operators have other licenses (comprehensive licence and bucket license).

Figure 5. Spectrum regulatory

Figure 6. Terminal regulatory

Figure 7. Operators licensing

Figure 8. Identified frequency allocation of regulators and existing solutions

- Interference issue

Concerning interference issue, regulators let the operator to manage by themselves and facilitate coordination to solve inter-operator interference. Meanwhile, operators do not use different spectrum to avoid interference issue.

Figure 9. Regulators interference management

Figure 10. Operators’ interference management

- Technical Challenge

Operators convince that the most technical challenge of deployment Femtocell is QoS management. Meanwhile, vendors convince that the most technical challenge of deployment Femtocell is interference management.

Figure 11. Technical challenge

- Backhaul type

Femtocell backhaul type solutions mostly support fast Ethernet and xDSL. Meanwhile, operators support all kind of backhaul link type (xDSL, FTTx).

Figure 12. Backhaul type

- Services of Femtocell

Operators and vendors convince that the basic service, data access and application, and location aware based service/application are service drivers to monetize Femtocell deployment.

Figure 13. Services of Femtocell

The complete results of questionnaire are reported as appendix of this document.

RESPONSES TO QUESTIONNAIRES ON FEMTOCELL

1. For Regulators

- Is there any Femtocell deployment or plan of deployment in your country? (please select one)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes, since (year) | Planned, will be deployed in (year) |  |
| Australia | ACMA |  |  | x | Planned, will be deployed in (year) Trials are currently underway with several operators, but no firm plans are known to the regulator on specific timeframes. |
| Japan | MIC |  | x |  | Since 2007 |
| China |  |  | x |  | Since 2009: Trial femtocell. The commercial time hasn’t been confirmed till now. |
| Brunei | AITI |  |  | x | Will be deployed in (year) 2012 |
| New Zealand | MED |  | x |  | Since 2010 |
| Korea | KCC |  | x |  | Since 2010 |

- Which Femto types those are deployed or intend to be deployed in your country? (you can select more than one answer)

Please describe your staging policy on Femtocell implementation:

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Femtocell (3GPP based), in year | Femtocell (CDMA2000 1xEVDO based), in year | Femtocell (WiMAX based), in year | Others |  |
| Australia | ACMA |  |  |  | x | It is likely that operators will deploy technologies that match the technology deployed in the band. In Australia, this is likely to be 3GPP or WiMAX based. Please describe your staging policy on Femtocell implementation: Current spectrum licence regulation allows operators to deploy femtocells in specific frequency and geographic areas; however, there is no specific staging policy implemented by the regulator. |
| Japan | MIC | x | x | x |  | To operate femtocell base stations by un-licensed person was permitted on October, 2008. Comprehensive license for femtocell base stations was permitted on March, 2011. Making possible reception through the Comprehensive licenses in place of separate licenses for femtocell base station on March, 2011. |
| China |  | x |  |  |  | In year 2009 (trial femtocell). Interference avoidance between Trial femtocell and macrocellular is the staging policy. Measure, test and verification are the most important tasks in this stage. |
| Brunei | AITI | x |  |  |  | In year 2012 |
| New Zealand | MED | x |  |  | x | This will be operarator determined |
| Korea | KCC | x |  | x |  |  |

- What kind of spectrum regulatory is currently applied for femtocell in your country? (you can select more than one answer)

Please mention the spectrum band used in your country for femtocell deployment:

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Un-licensed spectrum | Frequency Exclusivity Allocation | Others |  |
| Australia | ACMA |  |  | x | Unknown as trials are still being conducted. |
| Japan | MIC |  |  | x | Only the frequency band which is assigned for base stations of cellular phone services can be used by femtocell base stations. Spectrum band used in our country for femtocell deployment : The frequency band assigned for base stations of cellular phone service. (800MHz, 1.5GHz, 1.7GHz, 2GHz and 2.5GHz) |
| China |  |  |  | x | A spectrum band from 1975-1980/2165-2170MHz is allocated to operator for trial femtocelll. |
| Brunei | AITI |  | x |  | AITI has identified cellular bands for such systems and Operators providing such services require license called ’Infrastructure Provider for Telecommuncations Industry’ where the duration of license is 20 years. |
| New Zealand | MED |  |  | x |  |
| Korea | KCC |  | x |  |  |

- What kind of terminal regulatory is currently applied for femtocell in your country? (you can select more than one answer)

Please describe your policy:

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Type Approval of Equipment based on National Standard Specification | Unregulated | Others |  |
| Australia | ACMA |  |  | x | Must meet the requirements of the licence type |
| Japan | MIC | x |  |  |  |
| China |  | x |  |  |  |
| Brunei | AITI | x |  |  | All Radiocommunication equipments to be used in Brunei requires Type Approval and relevant Operational Licenses before implementation of such systems. |
| New Zealand | MED | x |  |  | A generic emmsion mask for transmissions |
| Korea | KCC |  |  |  | (none) |

- How many femtocell based products/services are currently operating in your country? Please describe for all types of products/services:

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Product/ Services | Cellular Operators | Wireline Operators |  |
| Australia | ACMA | Trials only |  |  |  |
| Japan | MIC | au femtocell | KDDI（au） |  |  |
|  |  | FOMA femtocell | NTT docomo |  |  |
|  |  | Home Antenna FT | Softbank mobile |  |  |
| China |  | Improve coverage in home, campus and business building | China Unicom | China Unicom |  |
| Brunei | AITI | None | None |  |  |
| New Zealand | MED |  |  |  | (none) |
| Korea | KCC | Voice/data | SKT |  |  |

- How do you manage interference issue caused by femtocell deployment?  (you can select more than one answer)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Let operators manage it | Implement strict Type Approval | Facilitate coordination to solve inter-operator interference | Others |  |
| Australia | ACMA | x |  |  |  |  |
| Japan | MIC |  | x | x |  |  |
| China |  |  |  |  | x | Femto test bands is not the same with macro cellular network’s. |
| Brunei | AITI | x |  | x | x | In the event that interference occurs, operators shall attempt to resolve amongst themselves, if issues cannot be resolved, AITI may facilitate inter-operator meetings to resolve their issues. |
| New Zealand | MED | x |  | x |  |  |
| Korea | KCC | x |  |  |  |  |

- Have you deployed or intend to regulate roaming issues on Femtocell? If so, please describe.  (you can select more than one answer)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, there is no intention on it | Still planning/ developing to regulate geographical roaming issues | Still planning/ developing to regulate inter-operator roaming issues. | Yes, there is regulation on geographical roaming issues since ( year) | Yes, there is regulation inter-operator roaming issues since ( year) | Others |  |
| Australia | ACMA | x |  |  |  |  |  |  |
| Japan | MIC | x |  |  |  |  |  |  |
| China |  |  |  |  |  |  | x | We are considering relevant policies. |
| Brunei | AITI | x |  |  |  |  |  |  |
| New Zealand | MED |  |  | x |  |  |  |  |
| Korea | KCC | x |  |  |  |  |  |  |

- Have you deployed or intend to regulate pricing issues on Femtocell? If so, please describe.  (you can select more than one answer)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, there is no intention on it | Still planning/ developing to regulate the bundled pricing issues. | Still planning/ developing to regulate inter-operator roaming issues. | Yes, there is regulation bundled pricing issues since ( year) | Yes, there is regulation cost structure on pricing issues since ( year) | Others |  |
| Australia | ACMA | x |  |  |  |  |  |  |
| Japan | MIC | x |  |  |  |  |  |  |
| China |  |  |  |  |  |  | x | We are considering relevant policies. |
| Brunei | AITI | x |  |  |  |  |  |  |
| New Zealand | MED | x |  |  |  |  |  |  |
| Korea | KCC | x |  |  |  |  |  |  |

- Have you deployed or intend to regulate interconnection issues on Femtocell? If so, please describe.  (you can select more than one answer)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, there is no intention on it | Still planning/ developing to regulate single cellular to multi wirelines interconnection issues | Still planning/ developing to regulate multi cellulars to single wireline interconnection issues. | Still planning/ developing to regulate multi cellulars to multi wirelines interconnection issues | Yes, there is regulation on single cellular to multi wirelines interconnection issues since ( year) | Yes, there is regulation on multi cellulars to single wireline interconnection issues since ( year) | Yes, there is regulation on multi cellulars to multi wirelines interconnection issues since ( year) | Others |  |
| Australia | ACMA | x |  |  |  |  |  |  |  |  |
| Japan | MIC | x |  |  |  |  |  |  |  |  |
| China |  |  |  |  |  |  |  |  | x | We are considering relevant policies. |
| Brunei | AITI | x |  |  |  |  |  |  |  |  |
| New Zealand | MED | x |  |  |  |  |  |  |  |  |
| Korea | KCC | x |  |  |  |  |  |  |  |  |

- How do you manage the spectrum / frequency allocation in terms of Femtocell?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Based on individual femtocell as in macrocell (per radio station licensing) | Based on spectrum band allocated for operator, and let the operator manage it | Release new spectrum for femtocell different with the macrocell one | Others |  |
| Australia | ACMA |  | x |  |  |  |
| Japan | MIC | x |  |  |  |  |
| China |  |  | x |  |  |  |
| Brunei | AITI |  | x |  |  |  |
| New Zealand | MED |  | x |  |  |  |
| Korea | KCC |  | x |  |  |  |

- How do you regulate QoS for Femtocell?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name |  |  |
| Australia | ACMA | QoS is operator specific and not a requirement set by the regulator. |  |
| Japan | MIC |  | (none) |
| China |  |  | (none) |
| Brunei | AITI | QoS regulatory framework for femtocell is not yet available. |  |
| New Zealand | MED | No regulation, Operator manages QoS |  |
| Korea | KCC |  | (none) |

2 For Operators

- Is there any Femtocell deployment or plan of deployment in your company? (please select one)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes, since (year) | Planned, will be deployed in (year) |  |
| Japan | EMOBILE Inc. | x |  |  |  |
| New Zealand | 2degrees mobile |  |  | x |  |
| Indonesia | TELKOM INDONESIA |  |  | x | will be deployed (year) 2012 |
| China | China Unicom |  |  |  | China Unicom is deploying femto in several cities, mainly focusing on indoor scenarios, and has no commercial plan yet. |
| China | China Telecom | x |  |  |  |
| China | CMCC | x |  |  |  |
| Korea | KT Corp |  |  | X |  |
| Korea | LG UPlus |  |  | X | 2013 |
| Korea | SK Telecom |  | x |  | 2010 |
| Japan | NTT DOCOMO |  | x |  | 2007 |
| Japan | KDDI Corp |  | x |  | 2010 |
| Japan | Softbank Mobile |  | x |  | 2009 |

- Which Femtocell types are deployed or intend to be deployed in your company? (you can select more than one answer)

| Responders | Answers | Please describe your policy |
| --- | --- | --- |
| Country | Organization Name | Femtocell (3GPP based), in year | Femtocell (CDMA2000 1xEVDO based), in year | Femtocell (WiMAX based), in year | Others |  |
| Japan | EMOBILE Inc. |  |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile | X |  |  |  |  |
| Indonesia | TELKOM INDONESIA | X |  |  |  | in year 2012 |
| China | China Unicom |  |  |  |  | China Unicom is deploying femto in several cities, mainly focusing on indoor scenarios, and has no commercial plan yet. |
| China | China Telecom |  | x |  |  | CMCC and CT are currently carrying out the research on Femtocell and some related experiments, but the plan of deployment has not been discussed yet. |
| China | CMCC |  |  |  | x | CMCC and CT are currently carrying out the research on Femtocell and some related experiments, but the plan of deployment has not been discussed yet. |
| Korea | KT Corp | x |  | x |  | Regulation issues should be solved first, then equipment cost should be lowered at a reasonable level for deployment |
| Korea | LG UPlus | x |  |  |  | Out of service area/ Taffic Offloading usede for in-building area |
| Korea | SK Telecom | x |  |  |  |  |
| Japan | NTT DOCOMO | x |  |  |  | The Femtocell was developed in order to expand area coverage into places such as small office home office (SOHO), and improve indoor or underground area coverage and user service quality. |
| Japan | KDDI Corp |  | x |  |  | 2010 |
| Japan | Softbank Mobile | x |  |  |  | Jan 2009 |

- What kind of regulatory licensing does your company hold?

| Responders | Answers | Please describe your policy: |
| --- | --- | --- |
| Country | Organization Name | Type Approval of Equipment/Standard Specification | Frequency Exclusivity Allocation | Others |  |
| Japan | EMOBILE Inc. |  | x |  |  |
| New Zealand | 2degrees mobile |  | x |  |  |
| Indonesia | TELKOM INDONESIA |  | x |  |  |
| China | China Unicom |  |  |  | Femto is in trial stage in China, licensing issue has not been decided yet. |
| China | China Telecom |  |  | x |  |
| China | CMCC |  |  | X |  |
| Korea | KT Corp |  | x |  |  |
| Korea | LG UPlus | x | x |  |  |
| Korea | SK Telecom |  |  | x |  |
| Japan | NTT DOCOMO | x |  | x | Comprehensive license |
| Japan | KDDI Corp |  |  | x | radio license for respective station in early stage, recently comprehensive license |
| Japan | Softbank Mobile | x |  | x | Bucket License |

- If you deployed or plan to deploy the femtocell; what kind of access method do you implement for your femtocell customers?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Close Access, only customers subscribed to the femtocell services | Open Access, all customers (with and/or wihout sucbription) from the same operator | Open Access, to all customers including other operator customers | Hybrid Access, priority to the femtocell customer and other customer (from the same operator) if there is unused capacity |  |
| Japan | EMOBILE Inc. |  |  |  |  | (none) |
| New Zealand | 2degrees mobile | x |  |  | x |  |
| Indonesia | TELKOM INDONESIA | x |  |  |  |  |
| China | China Unicom | x |  |  | x |  |
| China | China Telecom | x |  |  | x |  |
| China | CMCC |  | x |  | x |  |
| Korea | KT Corp |  |  |  |  | No decision yet made |
| Korea | LG UPlus |  | x |  |  |  |
| Korea | SK Telecom |  |  |  | x |  |
| Japan | NTT DOCOMO | x | x |  |  |  |
| Japan | KDDI Corp |  | x |  |  |  |
| Japan | Softbank Mobile |  | x |  |  |  |

- How do you control femtocell location?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Register the femtocell location prior to activation | Automatic location detection based on nearest macrocell id | Automatic location detection based on GPS information | Others |  |
| Japan | EMOBILE Inc. |  |  |  | x |  |
| New Zealand | 2degrees mobile |  | x |  |  |  |
| Indonesia | TELKOM INDONESIA | x | x |  |  |  |
| China | China Unicom |  | x |  |  |  |
| China | China Telecom |  |  |  |  |  |
| China | CMCC |  |  |  |  |  |
| Korea | KT Corp |  |  |  | x | No decision yet made |
| Korea | LG UPlus |  |  |  | x | Not decided yet |
| Korea | SK Telecom | x |  |  |  |  |
| Japan | NTT DOCOMO |  |  |  |  | (none) |
| Japan | KDDI Corp | x |  | x |  |  |
| Japan | Softbank Mobile | x |  |  |  |  |

- Do you allow your customer to move the femtocell location different from the initial registered location?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, the customer should report/re-registrate the femtocell | Yes, it can be moved only within the same cell id | Yes, it can be moved within the same city | Yes, it can be moved to the other cities within the country | Others |  |
| Japan | EMOBILE Inc. |  |  |  |  | x |  |
| New Zealand | 2degrees mobile | x |  |  |  |  |  |
| Indonesia | TELKOM INDONESIA |  |  |  |  | x | For time being still under assessment phase. |
| China | China Unicom |  |  |  | x |  |  |
| China | China Telecom | x |  |  |  |  |  |
| China | CMCC |  |  |  | x |  |  |
| Korea | KT Corp |  |  |  |  | x | No decision yet made |
| Korea | LG UPlus |  | x |  |  |  |  |
| Korea | SK Telecom | x |  |  |  |  |  |
| Japan | NTT DOCOMO | x |  |  |  |  |  |
| Japan | KDDI Corp | x |  |  |  |  |  |
| Japan | Softbank Mobile | x |  |  |  |  |  |

- Do you implement or plan to implement intra-operator roaming (customer able to access femtocell outside pre-registered femto zone)?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, the femtocell customers only access service in pre-registered femtocell group list | Yes, the femtocell customers may roam to any femtocell in CSG (Closed Subscriber Group) List | Yes, the femtocell customers may roam to any femtocell in Operator CSG List | Others |  |
| Japan | EMOBILE Inc. |  |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile | x |  |  |  |  |
| Indonesia | TELKOM INDONESIA | x |  |  |  |  |
| China | China Unicom |  | x |  |  |  |
| China | China Telecom |  |  |  |  |  |
| China | CMCC |  |  |  |  |  |
| Korea | KT Corp |  |  |  | x | No decision yet made |
| Korea | LG UPlus |  |  |  | x | Not decided yet |
| Korea | SK Telecom |  |  |  | x |  |
| Japan | NTT DOCOMO | x |  |  | x |  |
| Japan | KDDI Corp |  |  |  | x | No, on the intra-operator roaming. Any femtocell customer whose terminals are capable of cope with the femto station can make communication through the femtocell. |
| Japan | Softbank Mobile |  |  |  | x | Yes, All our customers may roam to any femtocell, Currently CSG is not used in our network. |

- Do you implement or plan to implement inter-operator roaming (customer able to access femtocell from other operator and vice versa)?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, it is closed to the femtocell customers, other operators’ customers are not allowed | Yes, customer from specific operator with roaming agreement can access the femtocell with open or hybrid access method | Yes, it is open for all operators customers with roaming agreement | Others |  |
| Japan | EMOBILE Inc. |  |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile | x |  |  |  |  |
| Indonesia | TELKOM INDONESIA | x |  |  |  |  |
| China | China Unicom | x |  |  |  |  |
| China | China Telecom |  |  |  |  |  |
| China | CMCC | x |  |  |  |  |
| Korea | KT Corp |  |  |  | x | No decision yet made |
| Korea | LG UPlus |  |  |  | x | Not decided yet |
| Korea | SK Telecom | x |  |  |  |  |
| Japan | NTT DOCOMO | x |  |  |  |  |
| Japan | KDDI Corp | x |  |  |  |  |
| Japan | Softbank Mobile |  |  |  | x | No, it is closed to our customers, other operators’ customers are not allowed |

- How do you manage interference issue between femtocell and macrocell?

| Responders | Answers | Please describe your policy: |
| --- | --- | --- |
| Country | Organization Name | Femtocell uses different spectrum | Intelligent femtocell (self-optimized) uses shared spectrum with macrocell | Femtocell uses a single carrier (i.e. f1), partially shared with macrocell carriers (f1, f2, f3) | Others |  |
| Japan | EMOBILE Inc. |  |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile |  | x |  |  |  |
| Indonesia | TELKOM INDONESIA |  | x | x |  |  |
| China | China Unicom |  |  |  | x |  |
| China | China Telecom |  |  |  |  |  |
|  | CMCC |  |  |  |  | CMCC: In the consideration of shortage of spectrum, intelligent share with macrocell is still in study for us. However, the effective method to avoid interference in the femtocell test is to use different spectrum. |
| Korea | KT Corp |  |  |  | x | No decision yet made. : Interference and Synchronization between Macro and Femto is one of the biggest obstacles needs to be solved in order to deploy femtocell. |
| Korea | LG UPlus |  |  |  | x | Not decided yet |
| Korea | SK Telecom |  |  | x |  |  |
| Japan | NTT DOCOMO |  | x | x |  |  |
| Japan | KDDI Corp |  |  |  | x | - The output power from the femtocell is limited to the level so as to accessible within the customer room and the station is requested to be placed away from the window. - Within the assigned frequency band the femtocell station selects a frequency slot in which the femtocell station is interfered as weak as possible. |
| Japan | Softbank Mobile |  |  | x |  |  |

- What is your main reason to implement Femtocell? (you can select more than one answer)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Handling more data capacity | Handling more voice capacity | Handling more data coverage | Handling more voice coverage | Offering more high speed on data | Minimizing the microcell and/or macrocell deployment cost | Others |  |
| Japan | EMOBILE Inc. | x |  | x |  |  | x |  |  |
| New Zealand | 2degrees mobile | x |  |  |  |  |  |  |  |
| Indonesia | TELKOM INDONESIA | x |  | x |  |  |  |  |  |
| China | China Unicom |  |  |  |  |  |  |  |  |
| China | China Telecom | x |  | x | x |  |  |  |  |
| China | CMCC | x |  | x | x |  |  |  |  |
| Korea | KT Corp | x |  | x |  |  |  |  |  |
| Korea | LG UPlus | x |  | x |  | x |  |  |  |
| Korea | SK Telecom | x |  |  |  | x |  |  |  |
| Japan | NTT DOCOMO | x |  | x | x | x |  |  |  |
| Japan | KDDI Corp |  |  | x | x |  |  |  |  |
| Japan | Softbank Mobile |  |  | x | x |  | x |  |  |

- Please select all applicable cost that are charged to your customer

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Terminal cost | Initial installation /registration cost | Femtocell monthly cost | Wireline broadband monthly cost | Femto-based services /application | Others |  |
| Japan | EMOBILE Inc. |  |  |  |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile |  |  |  |  |  |  | (none) |
| Indonesia | TELKOM INDONESIA |  |  | x |  |  |  |  |
| China | China Unicom |  |  |  |  |  |  |  |
| China | China Telecom |  |  | x | x | x |  |  |
| China | CMCC |  |  | x | x | x |  |  |
| Korea | KT Corp | x | x | x |  | x |  |  |
| Korea | LG UPlus |  |  |  |  |  | x | Not decided yet |
| Korea | SK Telecom |  |  |  |  |  | x |  |
| Japan | NTT DOCOMO |  | x | x | x |  | x |  |
| Japan | KDDI Corp |  |  |  | x |  | x | Usage fee of the femto station does not cost to the customer. |
| Japan | Softbank Mobile |  |  |  | x |  |  |  |

- How do you handle the end user pricing issues on Femtocell? If so, please describe.  (you can select more than one answer)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | The pricing is offered by wireline scheme and no additional cost for cellular | The pricing is offered by cellular scheme and no additional cost for wireline | There is a new pricing scheme | Others |  |
| Japan | EMOBILE Inc. |  |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile |  |  |  |  | (none) |
| Indonesia | TELKOM INDONESIA | x |  | x |  |  |
| China | China Unicom |  |  |  |  |  |
| China | China Telecom |  | x |  |  |  |
| China | CMCC |  | x |  |  |  |
| Korea | KT Corp |  |  |  | x | No decisions yet made |
| Korea | LG UPlus |  |  |  | x | Not decided yet |
| Korea | SK Telecom |  | x |  |  |  |
| Japan | NTT DOCOMO |  |  |  |  | Please refer to the answer to Question 11 |
| Japan | KDDI Corp | x |  |  | x | The additional cost for the use of the femto station is not born by the customers since the purpose is to provide cellular service even in the area where the radio strength is weak for the cellular terminal. |
| Japan | Softbank Mobile |  | x |  |  |  |

- Do you implement multivendor femtocell?

| Responders | Answers | Please describe your policy: |
| --- | --- | --- |
| Country | Organization Name | No, only a single vendor for femtocell | Yes, multivendor femtocells but single vendor for femtocell gateway | Others |  |
| Japan | EMOBILE Inc. |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile | x |  |  |  |
| Indonesia | TELKOM INDONESIA |  |  | x | Not yet implemented. |
| China | China Unicom |  |  |  | In our TD-SCDMA femtocell IOT test, multivendor femtocells and multivendor gateways are tested. We expect more vendors to join the TD-SCDMA femtocell industrial chain. |
| China | China Telecom |  | x |  |  |
| China | CMCC |  |  | x |  |
| Korea | KT Corp |  | x |  |  |
| Korea | LG UPlus |  |  | x | Not decided yet |
| Korea | SK Telecom |  |  |  | (none) |
| Japan | NTT DOCOMO |  |  |  | (none) |
| Japan | KDDI Corp | x |  |  |  |
| Japan | Softbank Mobile |  | x |  |  |

- Do you choose femtocell vendor different from the macrocell vendor?

| Responders | Answers | Please describe your policy: |
| --- | --- | --- |
| Country | Organization Name | No, femtocell vendor is the same with the macrocell | Yes, femtocell vendors are different with the macrocell vendor | Others |  |
| Japan | EMOBILE Inc. |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile |  |  | x | undecided |
| Indonesia | TELKOM INDONESIA |  |  | x | Not yet implemented |
| China | China Unicom |  |  |  |  |
| China | China Telecom |  |  | x | It depends on the femtocell stability, quality and technique support for us to choose vendor. Vendor who is the same with macrocell or not is acceptable. |
| China | CMCC |  |  | x |  |
| Korea | KT Corp |  | x |  |  |
| Korea | LG UPlus |  |  | x | Not decided yet |
| Korea | SK Telecom |  | x |  |  |
| Japan | NTT DOCOMO |  |  |  | (none) |
| Japan | KDDI Corp |  | x |  |  |
| Japan | Softbank Mobile |  | x |  |  |

- Do you manage multivendor femtocell interoperability test?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes |  |
| Japan | EMOBILE Inc. |  |  | (none) |
| New Zealand | 2degrees mobile |  |  | (none) |
| Indonesia | TELKOM INDONESIA | x |  | Not yet implemented |
| China | China Unicom |  |  |  |
| China | China Telecom |  | x | CT：the interoperability test is very important，but the test has not done yet. |
| China | CMCC |  | x | CMCC: the interoperability test is very important for multivendor femtocell deployment. To make sure the test quality and schedule, CMCC managed IOT test last year. |
| Korea | KT Corp |  | x |  |
| Korea | LG UPlus |  |  | Not decided yet |
| Korea | SK Telecom |  | x |  |
| Japan | NTT DOCOMO |  |  | (none) |
| Japan | KDDI Corp | x |  |  |
| Japan | Softbank Mobile |  | x |  |

- Do you control the femtocell specification?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, the femtocell specification is open and work with our network | Yes, we offer femtocell that fit with our requirement |  |
| Japan | EMOBILE Inc. |  |  | (none) |
| New Zealand | 2degrees mobile |  |  | (none) |
| Indonesia | TELKOM INDONESIA |  | x |  |
| China | China Unicom |  |  |  |
| China | China Telecom | x |  |  |
| China | CMCC | x |  | CMCC The femtocell specification is drafted in CCSA (China Communications Standards Association) and each vendor can offer the appropratie femtocell for CMCC. |
| Korea | KT Corp | x |  | KT participates in Femto Forum and other related bodies and SDOs. As common standard based femtocell should minimize the initial cost, this is the preferred way for KT. |
| Korea | LG UPlus |  |  | Not decided yet |
| Korea | SK Telecom |  |  | (none) |
| Japan | NTT DOCOMO |  |  | (none) |
| Japan | KDDI Corp |  | x |  |
| Japan | Softbank Mobile |  | x |  |

- What backhaul link (last mile) type do you support for femtocell?

| Responders | Answers | Please specify your typical bandwidth requirement for backhaul link: |
| --- | --- | --- |
| Country | Organization Name | xDSL | FTTx | Others |  |
| Japan | EMOBILE Inc. |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile |  |  |  | (none) |
| Indonesia | TELKOM INDONESIA | x | x |  |  |
| China | China Unicom | x | x | x |  |
| China | China Telecom | x | x | x |  |
| China | CMCC | x | x | x | CMCC does not possess the wireline licensing now. The broader bandwidth, the better we expect. |
| Korea | KT Corp |  |  | x | As KT has strong infrastructure for the backbone, there are many options for this. |
| Korea | LG UPlus |  |  | x | Not decided yet |
| Korea | SK Telecom |  | x |  |  |
| Japan | NTT DOCOMO |  | x |  |  |
| Japan | KDDI Corp | x | x | x | CATV |
| Japan | Softbank Mobile | x | x | x | Satelite Broad Band back hole |

- If you are cellular operator, do you have specific SLA with wireline operator?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, it is followed what customer’s SLA | Yes, it is controlled since the wireline operator from the same group | Yes, it is controlled by using special SLA | Others |  |
| Japan | EMOBILE Inc. |  |  | x |  |  |
| New Zealand | 2degrees mobile |  |  |  |  | (none) |
| Indonesia | TELKOM INDONESIA |  |  | x |  |  |
| China | China Unicom |  |  |  |  |  |
| China | China Telecom |  |  |  |  |  |
| China | CMCC |  |  | x |  |  |
| Korea | KT Corp |  | x |  | x | KT has both cellular and wireline. Hence this is not an issue. |
| Korea | LG UPlus |  | x |  |  |  |
| Korea | SK Telecom |  |  | x |  |  |
| Japan | NTT DOCOMO |  |  |  |  | (none) |
| Japan | KDDI Corp |  | x |  |  |  |
| Japan | Softbank Mobile | x |  |  |  |  |

- Is there any opinion or comment from your company on how to regulate the Femtocell services? If so please describe!

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes | Others |  |
| Japan | EMOBILE Inc. |  |  |  | (none) |
| New Zealand | 2degrees mobile |  |  |  |  |
| Indonesia | TELKOM INDONESIA |  | x |  | it should be soft regulated rather than based on strict regulation. |
| China | China Unicom |  |  |  |  |
| China | China Telecom |  |  |  |  |
| China | CMCC | x |  |  |  |
| Korea | KT Corp |  | x |  | Femtocell will use the same licensed spectrum and operate as part of the licensed operator’s existing network. In Korea, every BS needs inspection from the government and this ownership will regulate who is going to pay the cost for the inspection. Something needs to be done here regarding the regulations. |
| Korea | LG UPlus |  |  | x | Not decided yet |
| Korea | SK Telecom |  |  |  | (none) |
| Japan | NTT DOCOMO | x |  |  |  |
| Japan | KDDI Corp |  |  |  | (none) |
| Japan | Softbank Mobile | x |  |  |  |

- Please select services which are of your interest for current/future femtocell base implementation?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Basic service (voice, messaging) | Data access and applications | Location aware based services/applications | Machine-to-machine communication | IMS-based Services (with session management/ continuity) | Others |  |
| Japan | EMOBILE Inc. | x | x | x |  |  |  |  |
| New Zealand | 2degrees mobile | x | x |  |  |  |  |  |
| Indonesia | TELKOM INDONESIA |  |  | x | x | x |  |  |
| China | China Unicom |  |  |  |  |  |  |  |
| China | China Telecom | x | x | x |  |  |  |  |
| China | CMCC | x | x | x | x | x |  |  |
| Korea | KT Corp |  | x | x |  |  |  |  |
| Korea | LG UPlus | x | x | x | x | x |  |  |
| Korea | SK Telecom | x | x | x | x | x |  |  |
| Japan | NTT DOCOMO | x | x | x |  |  |  |  |
| Japan | KDDI Corp |  | x |  |  |  |  |  |
| Japan | Softbank Mobile | x | x | x | x | x |  |  |

- What kind of technical challenge do you experience?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Interference management | Self install devices | End-to-End QoS management | Backhaul quality | Others |  |
| Japan | EMOBILE Inc. | x |  |  | x |  |  |
| New Zealand | 2degrees mobile |  |  |  |  |  | (none) |
| Indonesia | TELKOM INDONESIA |  |  | x |  |  |  |
| China | China Unicom |  |  |  |  |  |  |
| China | China Telecom | x |  |  |  |  |  |
| China | CMCC |  |  |  |  | x | CMCC: Once after the remote upgrade, the femtocell could not connect the gateway. Another technical challenge is when femtocells roamed to other province, the KPI (Key Performance Indicator) of them are not monitored in BOSS (Business Operations Support System). |
| Korea | KT Corp | x |  |  |  |  | Macro to Femto interference issue is needed to be solved. |
| Korea | LG UPlus |  |  |  |  | x | Not deploy yet |
| Korea | SK Telecom | x | x | x | x |  |  |
| Japan | NTT DOCOMO | x | x | x | x |  |  |
| Japan | KDDI Corp | x | x | x |  |  |  |
| Japan | Softbank Mobile |  |  | x |  |  |  |

- Do you control the femtocell distribution?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, the femtocell can be purchased anywhere | Yes, customer can purchase the CPE from operator or sales-agencies |  |
| Japan | EMOBILE Inc. |  |  | (none) |
| New Zealand | 2degrees mobile |  |  | (none) |
| Indonesia | TELKOM INDONESIA |  |  | Not yet implemented. |
| China | China Unicom |  |  |  |
| China | China Telecom |  | x | Femtocell users need to sign an agreement with operator and we expect to arrange special engineer to install and open femtocell. |
| China | CMCC |  | x |  |
| Korea | KT Corp |  |  | As I have answered in 19. this should be based on the regulations. |
| Korea | LG UPlus |  |  | Not decide yet |
| Korea | SK Telecom |  |  | (none) |
| Japan | NTT DOCOMO |  |  | (none) |
| Japan | KDDI Corp |  | x |  |
| Japan | Softbank Mobile |  | x |  |

- How do you let your customer having the femtocell?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Buy from consumer electronic directly | Operator‘s customer/sales point and store | Others |  |
| Japan | EMOBILE Inc. |  |  | x | We have no deployment plan yet. |
| New Zealand | 2degrees mobile |  |  |  | (none) |
| Indonesia | TELKOM INDONESIA |  |  |  | Not yet implemented. |
| China | China Unicom |  |  |  |  |
| China | China Telecom |  |  |  |  |
| China | CMCC |  |  | x | CMCC: Now we think operator’s customer sales point or store is the way for customer to get a femtocell. The main consideration is that we can provide convenient register service at the same time. More over, we can also offer addtional installation service to help customer to choose a more approciate poisition for femtocell indoor coverage. |
| Korea | KT Corp |  |  | x | As I have answered in 19. this should be based on the regulations. |
| Korea | LG UPlus |  |  | x | Not deploy yet |
| Korea | SK Telecom |  |  | x | Installed by operator |
| Japan | NTT DOCOMO |  |  | x |  |
| Japan | KDDI Corp |  |  | x | Upon receiving request to improve area coverage from a customer, an operator installs a femtocell at customer premise if necessary. |
| Japan | Softbank Mobile |  |  | x | Web based application format is used. |

3. For Vendors

- Have you already produced Femtocell related products/solution offered to the telecom market? (please select one)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes | Planned |  |
| Singapore | Alcatel-Lucent |  | x |  | Since 2007 |
| China | HUAWEI |  | x |  | Since 2007 |
| China | DATANG |  | x |  | Since 2010 |
| China | ZTE |  | x |  | Since 2008 |
| Korea | LG Electronics | x |  |  |  |
| Korea | LG-Ericsson |  |  | x | 2012 |
| Korea | Samsung Electronics |  | x |  | 2005 |

- Which Femtocell types suit with your product / solution? (you can select more than one answer)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Femtocell (3GPP based), in year | Femtocell (WiMAX based), in year | Femtocell (CDMA2000 1xEVDO based), in year | Others |  |
| Singapore | Alcatel-Lucent | x |  |  |  |  |
| China | HUAWEI | x |  |  |  |  |
| China | DATANG | x |  |  |  |  |
| China | ZTE | x |  | x |  |  |
| Korea | LG Electronics |  |  |  |  | (none) |
| Korea | LG-Ericsson | x |  |  |  |  |
| Korea | Samsung Electronics | x | x | x |  |  |

- Please mention the operating frequency of your femtocell products?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name |  |  |
| Singapore | Alcatel-Lucent | 2.1GHz, 850, 1900Mhz and AWS |  |
| China | HUAWEI | For example, Huawei has products in the bands of 2100MHz and 1900MHz; however, Huawei can roll out corresponding products in line with the different market requests. |  |
| China | DATANG |  | (none) |
| China | ZTE | The frequency band for the products could be changed based on different systems such as UMTS, GSM, CDMA or customer’s different requirements. |  |
| Korea | LG Electronics |  | (none) |
| Korea | LG-Ericsson | AWS, 800MHz |  |
| Korea | Samsung Electronics | 1.9 GHz, 800 MHz |  |

- Do you think femtocell will become play important role in 4G indoor solution?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, Why? | Yes, Why? |  |
| Singapore | Alcatel-Lucent |  | x | The Femto cell benefits come as a result of many important aspects: ease of installation, lower cost backhaul, SoN, smaller cell radius and of course the ability to put the cell close to where the data usage is. In this case, installing a femto cell in indoors environments (e.g coffee shop) would avoid the inbuilding penetration loss and will ensure good signal coverage which result in better performance and enhanced customer experience. We see small cells playing a significant role in the 4G Radio Access Solution and forms a part of our ”lightRadio” RAN architecture. |
| China | HUAWEI | x |  | At current stage, femtocell is one of the options for the 4G indoor solutions in consideration by the mobile industry. |
| China | DATANG |  |  | (none) |
| China | ZTE |  | x | Because the data service is quite important for 4G systems, and the indoor application (enterprise&home) is the strongpoint for femtocell, compared with others, the volume and weight could be highlighted, furthermore, power and GPON transmit solution saves opearters’ CAPEX,etc.. |
| Korea | LG Electronics |  | x | As there are increasing demands from operators and end users on the usage of femto cell to improve the in-building reception quality and in-building data rate, forming basis for preferential services for end users |
| Korea | LG-Ericsson |  | x | Data offloading for indoor users |
| Korea | Samsung Electronics |  | x | Macro traffic offloading |

- Please rank of the following small cell solution for indoor coverage (from 1 to 5 where 1: the most important factor and 5: the less important)?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Femtocell | Picocell | Distributed antenna system | Repeater | Repeater/ relay base station |  |
| Singapore | Alcatel-Lucent | 1 | 3 | 2 | 5 | 4 |  |
| China | HUAWEI |  |  |  |  |  | In the different scenarios, different types of base stations could be applied. As a result, it is hard to rank the solutions. |
| China | DATANG |  |  |  |  |  |  |
| China | ZTE |  |  |  |  |  |  |
| Korea | LG Electronics |  |  |  |  |  | (none) |
| Korea | LG-Ericsson |  |  |  |  |  | (none) |
| Korea | Samsung Electronics |  |  |  |  |  | (none) |

- If you are femtocell supplier, please identify what kind of femtocell vendor you are, please select where applicable

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Femtocell and macrocell suplier | Femtocell and home gateway supplier | Femtocell only suplier | Others |  |
| Singapore | Alcatel-Lucent | x | x |  |  |  |
| China | HUAWEI | x |  |  |  |  |
| China | DATANG | x |  |  |  |  |
| China | ZTE | x |  |  |  |  |
| Korea | LG Electronics |  |  |  |  | (none) |
| Korea | LG-Ericsson | x |  |  |  |  |
| Korea | Samsung Electronics | x |  |  |  |  |

- Have you already deployed or intend to deploy your femtocell products through particular operators?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes, since (year) | Planned, will be deployed in (year) |  |
| Singapore | Alcatel-Lucent |  | x |  | since (year) 2008. Alcatel-Lucent has 17 customers worldwide and over 20 active trials. |
| China | HUAWEI |  | x |  | since 2008. Huawei has deployed femtocell products for many operators, such as StarHub, VDF Spain, China Unicom etc |
| China | DATANG |  |  | x | since (year) 2011 |
| China | ZTE |  | x |  | since 2008. ZTE has deployed enterprise femto networks for China Telefom, Telkomsel etc. |
| Korea | LG Electronics |  |  |  | (none) |
| Korea | LG-Ericsson | x |  |  |  |
| Korea | Samsung Electronics |  | x |  | 2005. customers : Sprint, Verizon |

- What is the main reason for your customers (operators) to deploy the femtocell? (please choose one for the most important driver)

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Indoor Coverage | Capacity Offload from macrocell to femtocell | Femto-based services | Low cost implementation | Others |  |
| Singapore | Alcatel-Lucent | x |  |  |  |  |  |
| China | HUAWEI | x | x |  |  | x | (Different customers have different motivation to deploy the femtocell.) |
| China | DATANG |  |  |  |  |  |  |
| China | ZTE |  |  |  |  |  |  |
| Korea | LG Electronics |  |  | x |  |  |  |
| Korea | LG-Ericsson |  | x |  |  |  |  |
| Korea | Samsung Electronics | x |  |  |  |  |  |

- Do you have any interoperability experience (femtocell access point in customers site and femto gateway in operators site) with other vendors?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name |  |  |
| Singapore | Alcatel-Lucent | We have conducted IOT with all the major core network suppliers for Femto gateway with different operators. We are planning to conduct the Iuh IOT with different vendors in upcoming Plugfest testing. ALU is part of Plugfest team of the FemtoForum and have participated in Plugfest #1 and Plugfest #2. |  |
| China | HUAWEI | The interoperability ability conforms to standard specifications. The femtocell could support gateway for the products from the same vendor, but for others,they may have problems now. |  |
| China | DATANG |  |  |
| China | ZTE |  |  |
| Korea | LG Electronics |  | (none) |
| Korea | LG-Ericsson | No |  |
| Korea | Samsung Electronics |  | (none) |

- Please describe your product status against open standard?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Our femtocell solution uses open standard Iuh specs and 3GPP specs, TR69 and TR196 | Our femtocell solution complies with open standard 3GPP | Our femtocell solution interoperables with other vendor all 6 major WCDMA core network vendors | Our femtocell solution holds certificate from independent test lab |  |
| Singapore | Alcatel-Lucent | x | x | x |  |  |
| China | HUAWEI | x | x |  |  | (femtocell solution is in compliance with the open standard, 3GPP HNB R8) |
| China | DATANG |  |  |  |  |  |
| China | ZTE |  |  |  |  |  |
| Korea | LG Electronics |  |  |  |  | (none) |
| Korea | LG-Ericsson |  | x |  |  | 3GPP Lite |
| Korea | Samsung Electronics |  |  | x |  |  |

- What kind of backhaul interface do you support?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Gigabit Ethernet | Fast Ethernet | xDSL | FTTx | Others |  |
| Singapore | Alcatel-Lucent | x | x | x | x | x | As long as the backhaul could provide Ethernet access for IP packet, all the above backhaul interfaces plus cable modem. |
| China | HUAWEI |  | x | x |  |  |  |
| China | DATANG |  |  |  |  |  |  |
| China | ZTE |  |  |  |  |  |  |
| Korea | LG Electronics |  |  |  |  |  | (none) |
| Korea | LG-Ericsson | x |  |  |  |  |  |
| Korea | Samsung Electronics |  |  |  |  |  | (none) |

- Does your product support self configure femtocell to allow plug and play installation?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes |  |
| Singapore | Alcatel-Lucent |  | x | Our solution support self configuration to allow true plug and play, this has been verified by many operators for commercial launch and lab/field trial testing. Network information and operator information are pre-loaded in the factory, the end user information is loaded into the system during the subscription provisioing, when the end user take the Femto home. The only thing required is to plug the Ethernet cable for the backhaul and power plug, then after a while the femto is ready to work. |
| China | HUAWEI |  | x |  |
| China | DATANG |  |  |  |
| China | ZTE |  |  |  |
| Korea | LG Electronics |  |  | (none) |
| Korea | LG-Ericsson |  | x |  |
| Korea | Samsung Electronics |  |  |  |

- How important is self optimization feature supported in femtocell product?

| Responders | Answers | Please describe: |
| --- | --- | --- |
| Country | Organization Name | Very important | Important | Not important |  |
| Singapore | Alcatel-Lucent | x |  |  | Self optimization features in Femto cell product will enable the min. interference with Macro layer, reduce the Opex for network optimization, as well as the end user experience is expected to be enhanced. |
| China | HUAWEI | x |  |  |  |
| China | DATANG |  |  |  |  |
| China | ZTE |  |  |  |  |
| Korea | LG Electronics | x |  |  |  |
| Korea | LG-Ericsson |  | x |  |  |
| Korea | Samsung Electronics |  | x |  |  |

- What kind of technical challenge do you think has become the most challanging issue in femtocell development?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Interference management | Self configure devices | QoS management | Backhaul | Others |  |
| Singapore | Alcatel-Lucent | x |  |  | x |  | Interference management >>> Interference mitigation in shared carrier deployment is an interesting topic to which ALU has developed a combination of techniques. Backhaul >>> Backhaul throughput in some Country in Asia is the major issue. |
| China | HUAWEI | x |  |  |  |  |  |
| China | DATANG |  |  |  |  |  |  |
| China | ZTE |  |  |  |  |  |  |
| Korea | LG Electronics |  |  |  |  |  | Different from the other cell types, femto cell is likely to be deployed without operators' direct intervention and hence it can incur a lot of uncontrollable interference to the surrounding network. Furthermore, basic operation mode of femto cell is likely to be ‘closed subscriber mode’ preventing users in the close vicinity of femto cell from handing over to it while interference from femto cell deteriorates communication quality from the original serving cell to the extent that proper communication is virtually impossible. Hence, appropriate interference management mechanism is crucial in order to maintain communication quality of users in the surrounding areas of femto cell. But, conventional interference management mechanisms based on the frequency domain coordination might not be applicable in case of femto cell deployment and hence some novel techniques may be required for intereference management. |
| Korea | LG-Ericsson |  | x |  |  |  |  |
| Korea | Samsung Electronics |  |  |  |  |  | (none) |

- Do you develop femtocell-based services?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No, only focus on femtocell devices | Yes |  |
| Singapore | Alcatel-Lucent |  | x | We have features that could be provided at Femto cell like local content sharing between handset and equipment at local network e.g., home PC, and also we could provide application program interface for operator to provide more value added service. Please refer to the Femtocell business case in the Attachment 2 for more information. |
| China | HUAWEI |  | x | At current stage, we primarily focus on femtocell devices; concerning the vision of femocell-based services, the market and operators requirements are the main driving force. |
| China | DATANG |  | x |  |
| China | ZTE |  | x |  |
| Korea | LG Electronics | x |  |  |
| Korea | LG-Ericsson | x |  |  |
| Korea | Samsung Electronics |  |  | (none) |

- Please select services you think become the major drivers to monetize femtocell deployment?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | Basic service (voice, messaging) | Data access and applications | Location aware based services/ applications | Machine-to-machine communication | IMS-based Services (with session management /continuity) | Others |  |
| Singapore | Alcatel-Lucent | x | x | x | x |  |  | Please refer to the Femtocell business case in the Attachment 2 for more information. |
| China | HUAWEI | x | x | x |  |  |  |  |
| China | DATANG |  |  |  |  |  |  |  |
| China | ZTE |  |  |  |  |  |  |  |
| Korea | LG Electronics |  | x |  |  |  |  |  |
| Korea | LG-Ericsson |  | x |  |  |  |  |  |
| Korea | Samsung Electronics | x | x |  |  |  |  |  |

- Do you have any opinion for a particular licensing issue for femtocell governed by your government?

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name | No | Yes |  |
| Singapore | Alcatel-Lucent |  | x | Administrations have recognized that adding new spectrum is not enough to address the mobile data traffic demand over the next 5 years. For example in January 2011, the FCC announced: “We need to encourage more innovative and efficient uses of spectrum. We’ll continue to encourage dynamic spectrum sharing and secondary markets for spectrum, as well as development and deployment of femtocells, smart antenna technology, and devices that can access unlicensed spectrum like Wi-Fi to off-load traffic from cellular networks.” Ref http://www.fcc.gov/Daily_Releases/Daily_Business/2011/db0120/DOC-304191A1.txt Femtocells are a new form of equipment, where the basestation function is formed into Customer Preimises Equipment (CPE). Hence local regulatory authorities need to treat there use as consumer equipment rather than a basestation as standard telecom equipment. The guiding princiles being; 1. Femtocells operate in and should comply with the operators existing spectrum allocation 2. Femtocells should be exempt for individual “basestation” type registration since their output power is similar to existing User Equipment (mobile handsets) 3. Femtocells should seek Type Approval for use in a consumer home/office environmen 4. Femtocells should be clasified such that they can be installed by the end-user 5. If neccessary clarification of regulations on the provision of emergency call location and national roaming access to emergency calls applied equally to femtocell users as to macrocell users. |
| China | HUAWEI |  | x | The main difficulty for femotcell application is interference issue; even though within the industry, there is in-depth discussion about the mitigation methods to be adopted, the interference issue is existed at much extent; provided there is particular license associated to femto, it would be a way out. |
| China | DATANG |  | x |  |
| China | ZTE |  | x |  |
| Korea | LG Electronics | x |  |  |
| Korea | LG-Ericsson | x |  |  |
| Korea | Samsung Electronics |  |  | (none) |

- How can your products support the spectrum / frequency allocation in terms of Femtocell? Please describe your solution.

| Responders | Answers | Notes |
| --- | --- | --- |
| Country | Organization Name |  |  |
| Singapore | Alcatel-Lucent | There are operator changable parameters which allocate the specific frequency for UL and DL for the femtocell to work within their licensed allocation, much like the standard mobile user devices. Because spectrum licenses can be geographically fragmented, we have implemented location and movement locking in our solution to ensure compliance to the licensing requirements. |  |
| China | HUAWEI | Depending on the operators’ requirements, the femtocell products could be designed in co-channel or non-overlapped with Marco. A good solution is dynamic/Semi-Dynamic frequency selection based on Femto Over the air listening. |  |
| China | DATANG |  |  |
| China | ZTE |  |  |
| Korea | LG Electronics |  | (none) |
| Korea | LG-Ericsson |  |  |
| Korea | Samsung Electronics |  | (none) |

3. For Other Institutions

# Is there any Femtocell deployment or plan of deployment in your country? (please select one)

| Responders | Answers |  |  | Notes |
| --- | --- | --- | --- | --- |
| Countries | Organization Name | No and there is no plan of Femtocell deployment (then answer no 2 only and no need to answer the rest of the questions) | Yes, since (year) | Planned, will be deployed in (year) |  |
| Korea | ETRI |  | x |  | 2011 |

# Do you have any opinion for particular licensing for Femtocell?

| Responders | Answers | Notes |
| --- | --- | --- |
| Countries | Organization Name | No | Yes |  |
| Korea | ETRI | x |  |  |

# Which Femtocell types are deployed or intend to be deployed in your country? (you can select more than one answer)

| Responders | Answers |  |  |  | Notes |
| --- | --- | --- | --- | --- | --- |
| Countries | Organization Name | Geographical roaming capability | Inter operator roaming capability | Flexible pricing handling | Others |  |
| Korea | ETRI |  |  | x |  |  |

# How many femtocell based products/services are currently operating in your country? Please describe for all types of product/service:

| Responders | Answers | Notes |
| --- | --- | --- |
| Countries | Organization Name | Type of product/services | Cellular Operators | Wireline Operators |  |
| Korea | ETRI |  | SK Telecom |  |  |

# What is the main benefit to use Femtocell? (you can select more than one answer)

| Responders | Answers |  |  |  |  |  |  | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Countries | Organization Name | Handling more data capacity | Handling more voice capacity | Handling more data coverage | Handling more voice coverage | Offering more high speed on data | Minimizing the microcell and/or macrocell deployment cost | Others |  |
| Korea | ETRI | x |  |  |  | x | x |  |  |

____________